## Slide 1: Announcements
This is the last week to decide your Research Report project
  Sign up on D2L
Today:
  Lecture on GPS mapping and use
  Lab using GPS devices

## Slide 2: GPS in the Field
Have you ever used a GPS device?
Why would you use one?
Notes: Who’s used a GPS before?
Why use it?
Confidence
Independent verification of location
Not as effective without traditional map and compass skills

## Slide 3: Why Use Geospatial Technology for Mapping?
Accuracy
Time
Overlays
Spatial Analysis
Modeling
Flexibility
Data Sharing
Notes: Hand mapping has more limited accuracy, can be more time consuming, and is hard to transfer to the computer.
GPS coordinates can transfer directly to computerized mapping, known as Geographic Information Systems (GIS), permitting overlay analysis and modeling.

## Slide 4: Brief History of GPS
  NavStar (now called GPS)
    Started development in 1973
      US military needs
    First four satellites launched in 1978
    Full Operational Capacity (FOC; July 17, 1995)
    System cost of $12 billion

## Slide 5: How it Works
Global Positioning Systems (GPS)
  Worldwide system of satellites, receivers, and software for
    Location: basic position
    Navigation: moving between positions
    Mapping: creating maps of the world
    Tracking: monitoring movement
    Timing: atomic-clock precision

## Slide 6: Divisions of GPS Technology
Three main segments
  Space (Satellite) Segment
  Ground Control Segment
  User (Receiver) Segment

## Slide 7: Satellite Segment
24+ satellites (normal constellation)
Extra back-up satellites
6 orbital planes
4 satellites / orbit
20,200 km altitude
12 hour orbit
Any given location avg of 9 satellites in range

## Slide 8: What it Looks Like

## Slide 9: Ground Control Segment
Ground stations located around the world monitor and maintain network of satellites
Master Control Station located in Colorado Springs, CO
http://www.gps.gov/systems/gps/control/

## Slide 10: Determining a Location
Determining horizontal position requires triangulation (technically trilateration):
  Need to know distance to at least 3 fixed objects (e.g., satellites, which orbit but have known locations at all times)
Determining vertical position (i.e., elevation) requires knowledge about position of a 4th fixed object
20,000 km
20,000 km
20,000 km
20,000 km
Notes: To provide an introductory description of how a GPS receiver works, errors will be ignored in this section. Using messages received from a minimum of four visible satellites, a GPS receiver is able to determine the times sent and then the satellite positions corresponding to these times sent. The x, y, and z components of position, and the time sent, are designated as where the subscript i is the satellite number and has the value 1, 2, 3, or 4. Knowing the indicated time the message was received , the GPS receiver can compute the transit time of the message as . Assuming the message traveled at the speed of light, c, the distance traveled or pseudorange, can be computed as .
A satellite's position and pseudorange define a sphere, centered on the satellite with radius equal to the pseudorange. The position of the receiver is somewhere on the surface of this sphere. Thus with four satellites, the indicated position of the GPS receiver is at or near the intersection of the surfaces of four spheres. In the ideal case of no errors, the GPS receiver would be at a precise intersection of the four surfaces.

## Slide 11: Determining a Location
2 satellites aren’t good enough …
Notes: To locate itself, a GPS receiver must find the distance to three satellites of known position. If the receiver finds that it is x miles from one satellite, it knows that it must be somewhere on an imaginary sphere, with the satellites as the center an a radius of x. If the receiver can generate these sphere for two satellites, it knows it can only be located where the surfaces of the two spheres intersect. The two spheres overlap in a ring of possible receiver positions.
By generating a sphere for a third satellite, the receiver narrows its possible position down to two points. The receiver dismisses the point located in space leaving only one possible position.

## Slide 12: What it Looks Like

## Slide 13: Selective Availability
Intentional degradation of publicly available GPS signals by the U.S. Department of Defense
  Purpose: deny ‘enemies’ access to highly accurate GPS data
  Errors of up to 100 m horizontally and 160 m vertically
  Turned off in May 2000

## Slide 14: Selective Availability
Longitude (m)
Latitude (m)
100
- 100
0
100
- 100
0
Selective Availability ON (05/01/00)
Longitude (m)
Latitude (m)
100
- 100
0
100
- 100
0
Selective Availability OFF (05/02/00)

## Slide 15: Error Sources
http://www.soi.wide.ad.jp/class/20050026/slides/01/61.html

## Slide 16: Local Base Stations to Correct Errors
http://ecrins2010.blogspot.com/
When PRECISION and ACCURACY really matter!
Fixed Station at ESRI headquarters

## Slide 17: Activity
2 minutes: Think about and write down ideas on how you might use GPS devices in your Research Report projects
  What would you locate, measure, or assess?
  What problems might you encounter?
2 minutes: Share these ideas with your neighbor and brainstorm a few new ones
Come together as a class to discuss ideas

## Slide 18: Using UTMs with GPS
Advantages:
  Constant distances across a map
    No distortion due to projection
  Values increase from zero in both X and Y
    No decimals or different ways of expressing values
  Values are in meters
    Metric system widely adopted
  Flat projection – no height considered
    Simple triangular calculations of distances
  = EASY TO UNDERSTAND

## Slide 19: What do you think?

## Slide 20: The UTM Grid
Wiki commons

## Slide 21: The UTM Grid
https://geoinfo.nmt.edu/publications/maps/gps/home.html

## Slide 22: The UTM Grid

## Slide 23
The UTM Grid

## Slide 24: Navigating the UTM Grid
Your coordinates:
  Easting: 543080 Northing: 3564700 Zone: 12S
You want to find:
  Easting: 519950 Northing: 3589360 Zone: 12S
You need to go:
  West 23130 m, and North 24660 m
  or (a2 + b2 = c2) 33809 m NW

## Slide 27: Today’s Lab
Navigate to waypoints
Calculate area
Graph features onto UTM grid
Note: Turn in 1 copy of lab per group.
Every student will turn in his/her own copy of Section 4 (map of restaurants)